Introduction Thesis

Variational Autoencoders are a Machine Learning method that adapts the general architecture of an autoencoder neural network to do Variational Bayesian Inference of a posterior distribution over the data.

For our purposes we are mainly interested in acquiring a generative model of the data P(X) as well as the structure of the underlying latent variables p(z) and the parameters of the functions mapping between the two.
A problem in approximating these distributions in the intractability in the standard marginal likelihood approach:
P(X) = ∫ P(X|z) P(z) dz
The problem here is that even when using sampling methods, most values of z have near-zero probability of having generated the data (P(X|z)≈0 for most z) so an intractably large number of z will need to be sampled to accurately approximate the correct distribution P(X).

A better approach would be to sample only from z that are likely to have produced X in the first place. A new function Q(z|X) could be used to find these samples. Q being an approximation of the distribution P(z|X), which is itself intractable in computations over datasets of a reasonable size (in the case of a continuous z it would need to calculate a possible distribution for all N datapoints). When sampling from a small number of likely z however, a highly similar distribution should be more easily computed by: Ez~Q P(X|z)

For the sake of convenience let us initially assume that the distributions Q is just some arbitrary distribution, not necessarily dependent on X.

The Kullback-Leibler divergence between this Q and the distribution Ez~Q P(X|z) would then be given by:

D[Q(z)||P(z|X)] = ∫ Q(z) log Q(z) – log P(z|X) dz
= Ez~Q [log Q(z) – log P(z|X) ]

Applying Bayes replaces the intractable term P(z|X) with P(X) and P(X|Z):
= Ez~Q [log Q(z) – log P(X|z) – log P(z) + log P(X) ]
= Ez~Q [log Q(z) – log P(X|z) – log P(z) ] + log P(X) (P(X) being independent of z~Q )

We can now rearrange the terms to move the independent P(X) to the left-hand side.
D[Q(z)||P(z|X)] - log P(X)	= Ez~Q [log Q(z) – log P(X|z) – log P(z) ]

Collapse log Q(z) and log P(z) into one KL divergence term:
D[Q(z)||P(z|X)] – log P(X)	= D[Q(z)||P(z) ] - Ez~Q[log P(X|z)]
log P(X) - D[Q(z)||P(z|X)]	= Ez~Q[log P(X|z)] - D[Q(z)||P(z) ]

At this point it does become useful to assume Q() depends on X, because replacing Q(z) with Q(z|X) now means that maximizing the left-hand side means increases the probability of the data P(X) and minimizing the KL divergence between the true and approximate distributions of Q(z|X) and P(z|X).
log P(X) - D[Q(z|X)||P(z|X)]	= Ez~Q[log P(X|z)] - D[Q(z|X)||P(z) ]

This optimizing can be performed on the two tractable terms on the right-hand side:
- increasing Ez~Q[log P(X|z)], analogous to increasing the probability of the encoded data given a sampled z (decoding probability)
- decreasing D[Q(z|X)||P(z)], analogous to reducing the error of the divergence between the approximated distribution Q(z|X) and true distribution P(z) (encoding error)

Optimizing these terms allows us to optimize P(X) in conjunction with D[Q(z|X)||P(z|X)] without having to deal with the intractable terms P(X|z) and P(z|X).
In other words:
log P(X)	= D[Q(z|X)||P(z|X)] + Ez~Q[log P(X|z)] - D[Q(z|X)||P(z) ]

D[Q(z|X)||P(z|X)] might be unknown, but it is by definition a non-negative term and so the two other terms count as a lower bound on the log probability of X. Optimizing this lower bound optimizes the data probability itself.

[ Because Jensen’s inequality states: f( E(X) ) >= E( f(X) ) if the function f is concave]
[Mention discrete inputs/ continuous latent space]

Lower bound
The lower bound terms can be interpreted from a Machine Learning perspective as two terms that together make up an autoencoder (i.e. a term for the loss of encoding the data X into the latent space z and a term for the probability of decoding a sample from the latent space back into data space) and would allow us to perform stochastic gradient descent if we define the loss on these terms correctly.

First let’s define the terms Q(z|X)and P(z) in the encoder D[Q(z|X)||P(z)]. For the sake of convenience we will assume both to be Gaussian distributions. We take P(z) to be a Gaussian distribution N(0,I) and Q(z|X) a Gaussian with the mu and Sigma determined by deterministic functions with parameters θ. The encoder loss takes for form D[N(mu(X),Sigma(X))||N(0,I) the solution to which can be calculated in closed form.

D[N(mu(X),Sigma(X))||N(0,I)]	= …
[derivation]

We can use a Neural Network as the deterministic function with parameters theta to find the mu and Sigma and consequently do gradient descent based on the loss function we have just defined.

Explanation of the reparametrization trick
The second lower bound term ( Ez~Q[log P(X|z)] – D[ Q(z|X)||P(z) ]) is a bit more difficult to implement. The sampling of z from distribution Q(z|X) is non-deterministic and makes it impossible to backpropagate the loss through gradients of the network before the sampling step. A way to make backpropagation through the mu and Sigma layers possible despite this sampling, is to take the sample not by taking a random value out of the distribution given by Sigma and mu, but rather to turn sampling into the multplication of the network N(mu,Sigma) with a random sample sample from distribution N(0,1) (i.e. e~ N(0,I)). By using this reparametrization trick the sample e can generate a sample by multiplying with Sigma followed by addition with mu. This approach makes it possible to calculate the gradients necessary for updating the mu and Sigma steps (through the addition and multiplication steps respectively) and leaves only the random sampling itself out of consideration when updating of the network weights.
[Illustration of the reparametrized sampling]
[Additional stuff concerning the Expectation?….]

With these specifications of the network both lower bound terms can be used to update the network and optimize the P(X). The network will be made up of an encoder and a decoder section. The encoder maps the input data to a latent distribution z by outputting a k-dimensional mean mu and diagonal covariance-matrix Sigma. These two values then calculate samples from the distribution by multiplying and adding to random sample e. Based on these samples the decoder network will then generate an output. The crossentropy between this output and the original input is then used to calculatet the second part of the loss function.

The loss function will consist of the addition of KL divergence of the distribution N(mu,Sigma) and the crossentropy loss between the input and output values:

L(Q,θ) + KL(Q||P)

[Illustration of network]

Mathematical similarity to EM-algorithm.
Bishop (9.4)/machinethoughts.
https://machinethoughts.wordpress.com/2017/10/02/vae-em/

The expectation maximization algorithm is a general technique for finding the maximum likelihood probability of a joint distribution of observed and latent variables given certain parameters θ.
The probability of the observed data is derived by marginalizing out the latent variables z:
P(X|θ)	=	P(X,Z|θ) / P(Z|θ)
or log prob:	ln P(X|θ)	=	ln P(X,Z|θ) - ln P(Z|θ)

which can be rewritten into:
ln P(X|θ)	=	∫ Q(Z) ln{ P(X,Z|θ) /Q(Z)} dz - ∫Q(Z) ln{P(Z|θ) / Q(Z)} dz
=	L(Q,θ) - KL(Q||P)
Now we seen two terms appear on the RHS that are very similar to the terms that are used for optimization in the VAE approach.
As the KL loss will be ≥0, optimizing the parameters of the lower bound L() increasing the data probability ln P(X|θ) alongside it.

The EM-algorithm now takes a two-step approach to optimization: Expectation and Maximization steps.
In the Expectation step the lower bound L(Q,θ) is maximized wrt Q(Z) while keeping the value of θ fixed. This is equivalent to setting the distribution Q(Z) equal to the posterior P(Z|X,θ) and making the KL divergence go to 0. At this point the lower bound is equal to the log likelihood.
Then in the Maximization step the the distribution Q(Z) is held fixed and the loss function L(Q,θ) is maximized wrt θ to give some new value θnew. The maximization step will also cause the lower bound to increase (unless it was already at maximum ) and the log likelihood with it.
[Figure 9.11 & 9.12 Bishop]

So the EM-algorithm is similar to VAE in that they both try to optimize the probability of the data X by maximizing the probability of the likelihood distribuiton and miniziming the KL divergence between the chosen distribution Q(Z) and real distribution P(Z).

The VAE algorithm however does this without being able to do the alternating updates of each distribution of the two wrt the other in closed form. Instead the VAE algorithm does gradient descent on the same objective funtion in those cases where the two distinct update steps are impossible.
Experiment Set-Up
Standard Seq-to-Seq set-up
The experiments on the VAE architecture are all variation on the VAE model by Bowman et al. (2016). This is a generative model that allows entire natural language sentences to be generated from a latent space representation.
Adapted to KB inputs
The first adaption to the standard framework is to apply it to a knowledge base (KB) instead of natural language. The knowledge base will be represented as a mapping all the possible knowledge statements to a vector. Each individual instance takes the form of a binary vector with 1’s for the statements that are true in this case and 0’s for the other (false) statements.
Mapping from one domain to the other
By using a parallel dataset of natural language and knowledge statements (Novikova et al. 2017) the natural language and KB VAE’s can be trained. The parallel corpus allows us to make use of the two latent representations and find ways of translating the representation in one domain to a representation in the other.
- Create a simple NN predictive model as baseline
For comparison with later adaptations of the VAE model it would be useful to create some model that maps natural language to knowledge statements and vice versa. As the knowledge statements are interpreted in this dataset as 1’s or 0’s over various knowledge categories, the model would in effect only be mapping to and from binary categories to character- or word embeddings.
- Maintain pretrained encoders/decoders, train a mapping from one latent space to another
After training the two individual VAE’s we can assume that the encoding to and from the latent representations are optimal and attempt to predict the latent representation in the parallel domain based on the values in the latent representation.
In essence the encoders and decoders are maintained and a [latent space]-to-[latent space] prediction model is trained to bridge the gaps between the two domains.
- Maintain a shared latent space between the two, train additional encoder/decoder models for mapping data to and from the latent representation in the other domain
If the two domains share a latent space, the two domains can be trained simultaneously. The inputs from the two domains are fed into two encoder networks who together generate the n-dimentional mu and sigma that the latent space is made up of. The samples from this space are then fed into two decoder models that map them back to the date space of the two domains